## Slide 1
TreeGuard
Smart IoT-Based Tree Health Monitoring System
Real-Time Monitoring of Tree Conditions Using IoT
1· K. VISHNU VARDHAN REDDY
2· L. NAGA HARSHITHA
3. L. SIVA LAKSHMI
4. CH.HARISH
B.Tech – Department of CSE · Kalasalingam Academy of Research and Education

## Slide 2
CHALLENGE
The Problem
Manual Inspection Only
Trees are commonly monitored through time-consuming, labor-intensive manual inspection.
Unnoticed Changes
Shifts in environmental conditions often go undetected between inspection cycles.
No Continuous Coverage
Early identification of unfavorable conditions is difficult without dedicated resources.
A simple IoT-based system for continuous and remote tree-environment monitoring is needed.

## Slide 3
Project Objectives
Monitor Continuously
Measure soil moisture, temperature, humidity, soil temperature, light, rainfall, and air quality — without interruption.
Collect & Process
Use the ESP32 microcontroller to read sensor data and manage data flow locally.
Transmit Wirelessly
Send data securely to the Blynk IoT cloud platform over Wi-Fi.
Alert Early
Identify abnormal environmental conditions early through configurable threshold-based notifications.

## Slide 4
SOLUTION OVERVIEW
Our Solution
Sensors → ESP32 → Wi-Fi → Blynk Cloud → Mobile Dashboard → Alerts
Sensors
Collect environmental data from tree surroundings
ESP32
Processes readings and manages data flow
Blynk Cloud
Live readings, graphs, and historical trends
Alerts
Configured thresholds trigger instant notifications

## Slide 5
Sensors Used
Professional product photos of the six sensor components used in the system.
Soil Moisture Sensor
Measures soil moisture levels around the root zone
DHT22
Measures ambient temperature and relative humidity
DS18B20
Measures soil temperature at root depth
BH1750
Measures light intensity in lux for photosynthesis monitoring
Rain Sensor
Detects rainfall and water presence on sensor surface
MQ-135
Indicates air quality and gas changes in the environment

## Slide 6
STACK
Hardware & Technology
Main Controller
ESP32 Development Board — Microcontroller with built-in Wi-Fi that processes sensor data and transmits to Blynk cloud.
Sensors & Components
Soil Moisture · DHT22 · DS18B20 · BH1750 · Rain Sensor · MQ-135
Breadboard, Jumper Wires, Power Supply (5V / 3.3V)
Software & Platform
Arduino IDE — Firmware development and deployment
Blynk IoT — Cloud connectivity and live visualization
Wi-Fi / Internet — Wireless data transmission

## Slide 7
ARCHITECTURE
System Architecture
Real-time Data Flow
Tree / Environment
Source of environmental parameters
Mobile Dashboard & Alerts
User visualization and notifications
Wi-Fi Network
Secure data transmission link
ESP32 Microcontroller
Data aggregation and preprocessing
Sensor Layer
Soil, DHT22, DS18B20, BH1750, Rain, MQ-135
Blynk Cloud Platform
Cloud storage and processing
Real-time environmental data flow from tree surroundings to the user
Tree / Environment
Source of all environmental parameters surrounding the tree
Sensor Layer
Six sensors capture soil, atmospheric, light, rain, and air quality data
ESP32 Microcontroller
Reads, processes, and manages all incoming sensor signals
Blynk Cloud
Receives data over Wi-Fi and stores it for dashboard and alerting
Mobile Dashboard
User-facing interface showing live readings, graphs, and alerts

## Slide 8
Working Principle
Sense Environment
Sensors detect surrounding conditions continuously
Collect Data
Raw readings gathered from all six sensors
Process Data
ESP32 processes and formats sensor values
Send to Cloud
Data transmitted wirelessly to Blynk platform
Monitor & Alert
Live dashboard displays readings and fires threshold alerts
TreeGuard continuously converts environmental conditions into real-time data for remote monitoring and early identification of abnormal conditions.

## Slide 9
PLATFORM
Blynk IoT Monitoring
Live Dashboard
Shows real-time sensor values using interactive widgets on mobile
Graphs & Trends
Visualizes sensor history and trend analysis for all parameters
Remote Access
Monitor tree conditions from anywhere via Internet connectivity
Threshold Alerts
Sends push notifications when defined conditions are exceeded
Monitored: Temperature · Humidity · Soil Moisture · Soil Temperature · Light Intensity · Rainfall · Air Quality

## Slide 10
VALIDATION
Experimental Testing & Results
Test Scenarios
Condition | Observed Behavior
Dry Soil | Low soil moisture readings
Wet Soil | High soil moisture readings
Normal Condition | Normal readings across all sensors
Higher Temperature | Temperature increase detected
Light Exposure | Change in light intensity measured
Rain / Water Contact | Rain detection triggered
Air Condition Changes | Change in MQ-135 output observed
Expected Results
✅ Real-time monitoring of all environmental parameters
✅ Wireless data transmission via Wi-Fi to Blynk cloud
✅ Live visualization and graphical analysis on mobile
✅ Detection of changing environmental conditions
✅ Configurable threshold-based alerts for abnormal conditions

## Slide 11
Conclusion & Future Scope
Key Achievements
1
Smart Monitoring
Continuous monitoring of environmental conditions around trees
2
Connected System
ESP32 collects and transmits data through Wi-Fi to Blynk
3
Remote Visibility
Real-time readings, graphs, and configurable alerts
4
Practical Solution
IoT-based approach to smarter environmental monitoring
Future Scope
1
AI Prediction
ML-based tree health and stress prediction
2
Smart Irrigation
Automatic irrigation triggered by soil moisture levels
3
Vision Detection
Camera and computer vision for disease detection
4
Large-Scale Monitoring
GPS-enabled multi-tree monitoring across campuses
TreeGuard transforms traditional tree monitoring into a connected IoT-based monitoring system.

## Slide 12
TreeGuard - Connecting Trees with Smart Technology

## Slide 13
THANK YOU
Questions & Discussion
We appreciate your time and attention.
Contact: hello@treeguard.com